## Slide 1: TRADITIONAL EARTHQUAKE-RESISTANT TECHNIQUES: THE CASBAH OF ALGIERS (ALGERIA)
Djillali BENOUAR and Amina FOUFA
USTHB
ALGERIA
Global Platform for Disaster Risk Reduction
Geneva, 22 May, 2013

## Slide 2: Algiers at the XVIIth century (After Daniel Stopendeal, towards 1680)

## Slide 3: CASBAH OF ALGIERS

## Slide 4: Archives
French files
(Consular courier 1716)
Arabic manuscript
(no date available)
Ottoman domanial act 1716

## Slide 5
IN THE WAKE OF 1716 ALGIERS EARTHQUAKE SEISMIC-RESISTANT TECHNIQUES CONCERNING THE FOLLOWING ASPECTS WERE IMPLEMENTED:
URBAN
ARCHITECTURAL
STRUCTURAL

## Slide 6
URBAN SCALE
THE BLOCKS : varying number of houses, are individualized by communication streets which surround them. This makes each block reacts independently from the others during the shakings.
THE HOUSES: are semi-detached, overlapping and leaning against each other forming a compact homogeneous unit.

## Slide 7
URBAN SCALE
THE SABATS: Number of streets are covered by galleries on top of which the houses extend and thus creating roofed passageways.
They can be flat with wooden logs incorporated or vaults built out of stones or bricks.

## Slide 8
URBAN SCALE:
DISCHARGING ARCHES: In urban framework, number of arches built out of stones or bricks. Allow transfer of horizontal loads to the ground.
Constructions are not isolated elements but compact dynamic block.

## Slide 9: DISCHARGING ARCHES

## Slide 10: DISCHARGING ARCHES

## Slide 12
ARCHITECTURAL SCALE:
TYPOLOGY OF HOUSES: Most of them have a central patio of square form around which the rooms are distributed (2 or 3 levels).
SHAPE OF HOUSE: Square form

## Slide 14
STRUCTURAL SCALE:
LINKS OF WALLS: Linked one to another by alternate crossing of wood logs (consolidating the angles). Every 50 cm in height, wood logs of about 2 m long.
PARTITIONS: Well connected to main walls by wood logs.

## Slide 15: STRUCTURAL SCALE:

## Slide 18: STRUCTURAL SCALE:
FLOORS: built by superposition of two layers of wood logs inserted in all width of bearing walls (rigid diaphragm).
CORBELLINGS: Frontal balcony overhanging and supported by wood logs forming an angle with bearing-wall.

## Slide 19: FLOORS

## Slide 20: CORBELLINGS

## Slide 22: CORBELLINGS

## Slide 23
STRUCTURAL SCALE:
OPENINGS: Wooden framing is found around the openings

## Slide 27: MOSQUE OF THE DEY

## Slide 28: MOSQUE OF THE DEY

## Slide 29: ARCH BUILT ON SHAKING TABLE (ENEA, ITALY)

## Slide 31
WANT TO SEE MORE….
VISIT THE CASBAH OF ALGIERS
THANK YOU VERY MUCH FOR YOUR ATTENTION